## Slide 1: UDS Services

## Slide 2: Contents
Why Diagnostic is needed ?
Introduction to UDS
Protocol Format
UDS Services

## Slide 3: Why Diagnostic Is Needed ?
To know the system failures and take corrective action
To know and modify the key parameters related to SW and HW.
Final level of IO testing could be performed using diagnostic.
Flashing and Re-flashing the application SW

## Slide 4: Why Diagnostic Is Needed ?
Tester request for ECU data or commands an action to ECU
ECU responds to tester request
Tester analyzes the data and concludes or take next action as per the request
TESTER
ECU
Request
Response

## Slide 5: Introduction to UDS
UDS is an abbreviation for Unified Diagnostic Services
UDS Define common requirements for diagnostic systems
UDS is defined by ISO (International Organization for standardization)
UDS occupies the 7th layer in ISO – OSI Model ,which is application Layer
UDS is independent of the physical link between client and server.
UDS frame data length has no limit but we know data length allowed at the CAN BUS is up to 8 byte. So data length greater then the allowed frame length must be segmented into multi-Frame as per CAN transport layer protocol(15765-2)before sending it at CAN-Bus.

## Slide 6: Protocol Format – Request & Response

## Slide 7: Service Identifiers Range

## Slide 8: The Sub-Function Byte of UDS
Services without Sub-Function-Byte:
  14, 23, 24, 2A, 2E, 2F, 34, 35, 36, 37, 3D, 84.
Services with Sub-Function Byte:
  10, 11, 19, 27, 28, 2C, 31, 3E, 83, 85, 87
Services with Sub-Function Byte and Storage State Parameter :
  86

## Slide 9: Some Commonly used NRCs

## Slide 10: UDS Services
Diagnostic and Communication Management functional unit
Data Transmission functional unit
Stored Data Transmission functional unit
Input/output Control functional unit
Routine functional unit
Upload Download functional unit

## Slide 11: Diagnostic and Communication Management functional unit
DiagnosticSessionControl (0x10) service
ECU Reset (0x11) service
Security Access (0x27) service
Communication Control (0x28) service
TesterPresent (0x3E) service
Control DTCSetting (0x85) service

## Slide 12: Data Transmission functional unit
ReadDataByIdentifier (0x22) service
WriteDataByIdentifier (0x2E) service
ReadMemoryByAddress (0x23) service
WriteDataByIdentifier (0x2E) service
ReadDataByPeriodicIdentifier (0x2A) service
DynamicallyDefineDataIdentifier (0x2C) service

## Slide 13: Stored Data Transmission functional unit
ClearDiagnosticInformation (0x14) Service
ReadDTCInformation (0x19) Service

## Slide 14: Routine functional unit
RoutineControl (0x31) service

## Slide 15: Input/output Control functional unit
InputOutputControlByIdentifier (0x2F) service

## Slide 16: Upload Download functional unit
Request Download (0x34) service
Request Upload (0x35) service
Transfer Data (0x36) service
Request Transfer Exit (0x37) service
Request File Transfer (0x38) service

## Slide 17: Diagnostic Session Control (0x10) service
The Diagnostic session control service is used to enable the different diagnostic session in the service.
A diagnostic session enables a specific set of diagnostic service and /or functionality in the service.
At a time only one diagnostic session active in a server. Default session shall be run as long as the server is powered up.

## Slide 18: DiagnosticSessionControl (0x10) service
Default session (01)
Programming session (02)
Extended session (03)

## Slide 19: What does a Diagnostic session describe?
Applicable services
Amount of functionality
Timing parameter values

## Slide 20: Different Sessions
  Default session
  No tester present required to keep the session active
  Does not support any diagnostic application timeout provision
  Does not require security capability
Programming session
  All diagnostic services required to support memory programming of ECU

## Slide 21: Different Sessions
Extended session
  Enables all diagnostic services supported by individual ECU. Timer controlled environment for ECU in which all of the supported diagnostic services can be executed. All diagnostic services are supported in extended diagnostic session (some are with security features and must be unlocked before use)

## Slide 22: DiagnosticSessionControl (0x10) service

## Slide 23: Diagnostic Session Control (0x10) service - subfunctions

## Slide 24: DiagnosticSessionControl (0x10) service
P2 Server : Default P2Server_max timing supported by the server for the activated diagnostic session.
P2*Server_max : Enhanced (NRC 0x78) P2Server_max supported by the server for the activated diagnostic session.
S3 Server Time out : session time out

## Slide 25: Diagnostic Session Control (0x10) service
All requests sent by the Tester will expect a positive response or a RCRRP (Request Received Response Pending) with in 50ms as mentioned in the table below. The timings which ever are greater than 50ms have to support RCRRP Message

## Slide 26: DiagnosticSessionControl (0x10) service – Function Execution Time
Service ID | Name | 0x01(ms) | 0x02(ms) | 0x03(ms)
0x10 | Diagnostic Session Control | 50 | 25 | 50
0x11 | ECU Reset | 200 | 200 | 200
0x14 | Clear Diagnostic Information | 1000 |  | 1000
0x18 | Read DTC Information | 50 |  | 50
0x22 | Read Data by Identifier | 50 | 25 | 50
0x27 | Security Access | 50 | 25 | 50
0x2E | Write Data by Identifier | 5000 | 5000 | 5000
0x31 | Routine Control | 200 | 60000 | 200
0x2F | Input Output Control by Identifier | 50 |  | 50
0x34 | Request Download |  | 1000 | 
0x36 | Transfer Data |  | 5000 | 
0x37 | Transfer Exit |  | 5000 | 
0x3E | Tester Present | 50 | 25 | 50
0x85 | Control DTC Setting | 200 |  | 200

## Slide 27: Diagnostic Session Control (0x10) service
The following NRC’s are supported
  0x12 - sub function Not Supported
  0x13 - incorrect Message Length Or Invalid Format
  0x22 - conditions Not Correct

## Slide 28: ECU Reset (0x11) service
The ECU Reset is used by the client to request a server reset.
This service request the server to effectively perform a server reset based on the content of the reset type parameter values embedded in the ECU Reset request messages
Different Reset Types :
HARD Reset ,Soft Reset ..etc.

## Slide 29: ECUReset (0x11) service
Hard Reset:
  Server Power shut down(battery removed) followed by the power-up sequence is known as “Hard Reset”.
  There is no standard action performed during hard-reset command it is completely application Specific.
  A hard reset might end with the re-initialization of volatile and non-volatile memory.
Key Off-On Reset:
  As the name suggests, this command is like off the ignition and then again on.
  Like other resets there is nothing to do standard for this value, all is implementation specific.
  Volatile memory re-initialized but Non-volatile data will remain protected.

## Slide 30: ECU Reset (0x11) service
Soft Reset:
  A server will not completely shut down when soft reset will receive. It will just restart the application.
  Like the Hard reset, No standard action performed in Soft reset. It is implementation specific.
  Soft reset might end with the volatile data clear but Non -Volatile data will be preserved

## Slide 31: ECU Reset (0x11) service

## Slide 32: ECU Reset (0x11) service
The following NRC’s are supported
  0x12 - sub function Not Supported
  0x13 - incorrect Message Length Or Invalid Format
  0x22 - conditions Not Correct
  0x33 – security Access Denied

## Slide 33: Security Access (0x27) service
The Security access is used to provide access to data and/or services that have restricted access.
Security Access requires the transmission of two requests:
1. Request the Seed
2. Send the Key.

## Slide 34: Security Access (0x27) service

## Slide 35: Security Access (0x27) service
Flow of the Security Access(27h) service is as follows :
  Client requests the “seed”;
  Server sends the “seed”;
  Client sends the “key” (appropriate for the Seed received);
  Server responds that the “key” was valid and that it will unlock itself.

## Slide 36: Security Access (0x27) service

## Slide 37: Security Access (0x27) service
The following NRC’s are supported
  0x12 - sub-function Not Supported
  0x13 - incorrect Message Length Or Invalid Format
  0x22 - conditions Not Correct
  0x31 – request out of Range
  0x33 – security Access Denied
  0x35 - invalid Key

## Slide 38: Security Access (0x27) service
0x36 - Exceeded Number Of Attempts
0x37 - Required Time Delay Not Expired

## Slide 39: Communication Control (0x28) service
This service shall be used to switch on/off the transmission and/or reception of CAN messages
To run this service the server shall be in extended diagnostic session only.
Different Sub function
  00h – enable Rx and Tx
  01h – enable Rx and Disable Tx

## Slide 40: Communication Control (0x28) service
02h – Disable Rx and Enable Tx
03h – Disable Rx and Tx

## Slide 41: Communication Control (0x28) service

## Slide 42: Communication Control (0x28) service

## Slide 43: Communication Control (0x28) service
The following NRC’s are supported
  0x12 - sub function Not Supported
  0x13 - incorrect Message Length Or Invalid Format
  0x22 - conditions Not Correct
  0x31 – Request out of range

## Slide 44: Control DTC Setting (0x85) service
The ControlDTCSetting service shall be used to disable/ re-enable the setting of diagnostic trouble codes in ECU
Sub function :
- On (01) – Allow DTC Setting
- Off (02) – Stop DTC Setting

## Slide 45: Control DTC Setting (0x85) service

## Slide 46: Control DTC Setting (0x85) service
The following NRC’s are supported
  0x12 - sub function Not Supported
  0x13 - incorrect Message Length Or Invalid Format
  0x22 - conditions Not Correct
  0x31 – Request out of range

## Slide 47: Tester Present (0x3E) service
This service shall be used to keep the ECU in a diagnostic session other than the default Session. It may also be used to inform the ECU that the “Off Board Tool” is still connected and certain diagnostic services and/or communication remain active
This request is sent by client periodically.

## Slide 48: Tester Present (0x3E) service
Sub Function :
  - zero sub function
  - suppress positive response

## Slide 49: Tester Present (0x3E) service

## Slide 50: Tester Present (0x3E) service
The following NRC’s are supported
  0x12 - sub function Not Supported
  0x13 - incorrect Message Length Or Invalid Format

## Slide 51: Read Data By Identifier (0x22) service
This service allows the tool to request data record values from the ECU via the predefined data Identifiers.
This service is generally used to get logistic data like part numbers, configuration parameters and also vehicle parameters.

## Slide 52: Read Data By Identifier (0x22) service

## Slide 53: Read Data By Identifier (0x22) service
The following NRC’s are supported
  0x12 - sub function Not Supported
  0x13 - incorrect Message Length Or Invalid Format
  0x22 - conditions Not Correct
  0x31 – Request out of range
  0x33 - security Access Denied

## Slide 54: Read Data By Identifier (0x22) service

## Slide 55: Write Data By Identifier (0x2E) service
The Write Data By Identifier service allows the client to write information into the server at an internal location specified by the provided data identifier.
The Write Data By Identifier service is used by the client to write a data Record to a server. The data is identified by a data Identifier, and may or may not be secured

## Slide 56: Write Data By Identifier (0x2E) service

## Slide 57: Write Data By Identifier (0x2E) service
The following NRC’s are supported
  0x12 - Sub function Not Supported
  0x13 - Incorrect Message Length Or Invalid Format
  0x22 - Conditions Not Correct
  0x31 - Request out of range
  0x33 - Security Access Denied
  0x72 - General Programming Failure

## Slide 58: Write Data By Identifier (0x2E) service

## Slide 59: Need for Service 0x31 – Routine Control
The Routine Control service is used by the client to execute a defined sequence of steps and obtain any relevant results.
Common usages are erasing memory, resetting or learning adaptive data, running a self-test, overriding the normal server control strategy, and controlling a server value to change over time including predefined sequences etc.

## Slide 60: Routine Control (0x31) service

## Slide 61: Routine Control (0x31) service – Routine control types
Routine Control Types
  Start Routine (01 hex)
  Stop Routine (02 hex)
  Request Results (03 hex)

## Slide 62: Routine Control (0x31) service

## Slide 63: Routine Control (0x31) service
The following NRC’s are supported
  0x12 - sub function Not Supported
  0x13 - incorrect Message Length Or Invalid Format
  0x22 - conditions Not Correct
  0x24 – Request Sequence Error

## Slide 64: Routine Control (0x31) service
0x31 – Request out of range
0x33 - security Access Denied
0x72 - general Programming Failure

## Slide 65: Input/output Control functional unit – Service 2F
The InputOutputControlByIdentifier service is used by the client to substitute a value for an input signal, internal server function and/or force control to a value for an output (actuator) of an electronic system.
In general, this service is used for relatively simple (e.g., static) input substitution / output control whereas routine Control is used if more complex input substitution / output control is necessary.

## Slide 66: Input/output Control functional unit – Service 2F
ECU shall re-assume control over the outputs previously under control of the external test tool if one of the following conditions are met:
  A request to Return control to the ECU
  A session transition occurs
  A ECU reset occurs
  Internal disable conditions

## Slide 67: Service 2F NRCs
0x13 – Incorrect Message length or Invalid format
0x22 – Conditions not correct
0x31 - Request Out of range
0x33 – Security Access denied

## Slide 68: Service 2F