## Slide 1: Design Patterns for Embedded Systems (Part 1)

## Slide 2: Topics
Embedded Systems – definition
Real time systems
Embedded toolchains
OS, RTOS or bareback?
Debugging
Testing
Testing strategies
OO or structured?

## Slide 3: Definition of Embedded Systems
“A computerized system dedicated to performing a specific set of real-world functions rather than to providing a generalized computing environment.”
Many embedded systems have no disks, human interface, and barely any memory.

## Slide 4: Examples
In the medical field, embedded systems include implantable devices (e.g., cardiac pacemakers, defibrillators, and insulin pumps), monitoring equipment (e.g., ECG/EKG monitors, blood gas monitors, blood pressure monitors, EMG monitors), imaging systems (e.g., CT, SPECT, PET, TEM, and x-ray imagers), and therapy delivery devices (e.g.,patient ventilator, drug vaporizers, and infusion pumps).
In the telecom market, there are devices ranging from cell phones, switching systems, routers, modems, and satellites.
In the office, embedded systems manage phones, printers, copies, fax machines, lights, digital projectors, security systems, and fire detection and suppression systems.

## Slide 5: Examples
In automotive environments, embedded systems optimize engine combustion, manage power delivery in transmissions, monitor sensor data, control anti-lock braking, provide security, and offer infotainment services such as CD and DVD players, and GPS routing (in some locations, they can offer radar and laser detection and even active radar and laser countermeasures).
In the home, examples include ovens, televisions, radios, washing machines, and even some vacuum cleaners.

## Slide 6: Examples

## Slide 7: Real time systems
An important subset of embedded systems are real-time systems.
“real time” is not “real fast”.
A real-time system is one in which timeliness constraints must be satisfied for system correctness.
Categorization of real-time systems is into two groups.
“Hard” real-time systems are ones in which timeliness constraints are modeled as deadlines, points in time by which the execution of specific actions are required to be complete.

## Slide 8: Real time systems
“Soft” real-time systems are those that are not “hard”; that is, some other (usually stochastic) measure than deadlines is used to determine timeliness. This may include average throughput, average execution time, maximum burst length, or some other measure.
All systems may be modeled as hard real-time systems, but this often results in “over-designing” the system to be faster or have more available resources than is necessary, raising the recurring cost (approximately “manufacturing cost”) of the system.
The primary reason for modeling real-time systems as “hard” is because it eases the assurance of the system’s timeliness through mathematical analysis.

## Slide 9: Embedded Design Constraints
An embedded system is usually shipped already integrated with all the hardware it needs.
The hardware platform is not usually user-extensible, so resources such as memory, power, cooling, or computing power contribute to the per-unit cost (known as recurring cost).
To maintain profitability, there is almost always tremendous pressure on the developer to minimize the use of such hardware resources.
So Embedded systems often require additional optimization efforts.

## Slide 10: Embedded Design Constraints
Performance concerns are often critical to the success of a system.
There are many aspects to performance, in some systems, throughput is a critical criterion.
Throughput is normally measured in terms of the number of transactions, samples, connections, or messages that can be processed per unit time. In other systems, handling each request as quickly as possible is more important, a quality known as responsiveness, usually captured as a worst case execution time.
Other systems value predictability of performance over maximum throughput or responsiveness.
Predictability is usually measured as occurring within a range or as being drawn from a probability density function.

## Slide 11: Embedded Design Constraints
Reliability, robustness, and safety are other kinds of constraints levied on embedded systems.
The reliability of a system is a (stochastic) measure of the likelihood that the system will deliver the correct functionality.
Robustness refers to the ability of a system to deliver services properly when its preconditions (such as operating conditions or input data rates) are violated.
Safety denotes the level of risk of a system, that is, the likelihood that using the system will result in an accident or loss.
These concerns often require additional hardware and software measures to maintain the operation of the system within acceptable limits. For example, most embedded systems have a power on self-test (POST) as well as a periodic or continuous built-in test (BIT).

## Slide 12: Embedded Toolchain – Cross Compiler
Most embedded systems are created on a different system (the “host”) than they execute on (the “target”).
The most obvious such tool is the cross-compiler. This is a compiler that runs on the host but creates executable code that runs on a different computer and operating environment.
Many real-time operating systems (RTOSs) provide their own proprietary compilers or provide customizations for open-source compilers such as GCC (Gnu Compiler Collection).

## Slide 13: Embedded Toolchain - Linker
A linker is a program that combines a set of executable codes together into an executable for a target.
Most embedded OSs require an explicit linking step.
The linker often relocates the program as well, meaning that the start address is specified during the link step and assembly language jump instructions must be updated to reflect the actual starting base address.

## Slide 14: Embedded Toolchain - Loader
A loader is a tool that loads the object image output from the linking step into the memory of the target environment.
This may be done via a serial or network link or by burning the software image into nonvolatile memory such as Flash or EPROM.
As an alternative to loading the software image on a target platform, many developers use simulators for the target that execute on their host development systems.

## Slide 15: Embedded Toolchain - Debuggers
The next set of tools are debuggers – tools that give us a great measure over the execution of the software, including the ability to step into (execute line by line) or step over (execute in entirety) functions, set breakpoints, and to examine and modify variables. These debuggers may work over standard serial and network links or over JTAG ports.
Modern-day Integrated Development Environments (IDEs) link together most or all of the tools in the embedded tool chain to facilitate and automate the development process. The latest industry trend is to host the IDEs in the Eclipse platform because of the power of the integrated environment and the availability of third-party and open-source plug-ins

## Slide 16: OS, RTOS or bareback?
An operating system (OS) provides a set of system and platform execution services for the application developer, especially around the management and use of target system resources.
These resources include memory, concurrency units (processes, tasks, or threads), event queues, interrupts, hardware, and application programs.
Most OSs do not provide any guarantees about timeliness, and desktop OSs may invoke unpredictable delays due to internal processing, memory management, or garbage collection at unforeseeable times.
This unpredictability, and the fact that most desktop OSs are huge (compared to available memory), makes them unsuitable for real-time and embedded environments that are constrained in both time and resources.

## Slide 17: OS, RTOS or bareback?
A real-time operating system (RTOS) is a multitasking operating system intended for real-time and embedded applications.
RTOSs are generally written to provide services with good efficiency and performance, but usually the predictability of the performance is more important than the maximum throughput.
RTOSs are smaller and often less capable than desktop OSs.
RTOSs don’t guarantee real-time performance but they provide an application environment so that appropriate developed applications can achieve real-time performance.

## Slide 18: OS, RTOS or bareback?
RTOSs run applications and tasks using one of three basic design schemas.
Event-driven systems handle events as they arise and schedule tasks to handle the processing.
Most such systems use task priority as a quantitative means by which to determine which task will run if multiple tasks are ready to run.
Task priorities are most often static (i.e., specified at design time as such with rate-monotonic scheduling) but some are dynamic, varying the task priorities to account for current operating conditions (such as earliest deadline first scheduling).
The other two approaches to task scheduling implement a “fairness doctrine” either by giving all tasks a periodic time slice in which to run (time-base schemas, such as round robin scheduling) or by running the task set cyclically (sequence-based schemas, such as cyclic executive scheduling).

## Slide 19: OS, RTOS or bareback?
Some systems having too few resources to support both an RTOS and the actual application software opt to go bareback – that is, function without a commercial or proprietary RTOS at all.
This means(bareback code) that the application code itself must replicate any RTOS services or functionality needed by the application.
This is needed to add the additional complexity of behavior required in modern embedded devices and is enabled by the lower recurring costs of parts and manufacturing.
For very simple embedded systems, there may be no explicit operating system functionality at all.

## Slide 20: OS, RTOS or bareback?
The application may simply be a set of interrupt handlers that communicate via a shared resource scheme such as queuing or shared memory.
Alternatively, a simple task loop implementation of a cyclic executive might suffice. Somewhat more complex systems may introduce operating system features such as memory or task management as they need them.
From one point of view, an operating system is an integrated set of design patterns that provides certain kinds of services and resources to applications.

## Slide 21: Debugging and testing – Test Driven Development
The state of the art in developing defect-free software is an agile practice known as test-driven development (TDD).
In TDD, the unit tests for a piece of software are written simultaneously with, or even slightly before, the software it will verify.
The unit and integration tests are performed frequently during the coding phase, thus ensuring rigorous and comprehensive testing.
It forces the developer to plan the unit and understand the specification completely before coding.
This way code is more optimized and defect injections from poor ad hoc planning are prevented

## Slide 22: Debugging and testing – Test Driven Development
It offers very high test coverage and leads to modular design.
TDD results in high quality basic modules that help establishing high quality system that requires less high-level testing, thus having positive influence on total project time.

## Slide 23: Debugging and testing – Test Driven Development
TDD amount of time saved in later testing phases, debugging and code fixing is unsurpassed, not to mention the increase in quality and reliability.
The operations of embedded systems rely heavily on the real-time events in the plant and the embedded environment itself. Therefore it is advisable to favor bottom-up method for TDD, since writing stubs simulating the real-time events is difficult and even redundant when the complexity of stubs approach the complexity of the module they are simulating.
Nevertheless, the structure and functions of the system are the main features that dictate the best TDD approach for the project.

## Slide 24: Different Unit tests
Functional – tests the behavior or functionality of a system or system element
Quality of Service – tests the “performance” of a system or system element, often to measure the performance of the system or element against its performance requirements
Precondition tests – tests that the behavior of the system or system element is correct in the case that the pre-conditional invariants are met and in the case that the pre-conditional invariants are violated
Range – tests values within a data range
Statistical – tests values within a range by selecting them stochastically from a probability density function (PDF)

## Slide 25: Different Unit tests
Boundary – tests values just at the edges of, just inside, and just outside a data range.
Coverage – tests that all execution paths are executed during a test suite.
Stress – tests data that exceeds the expected bandwidth of a system or system element.
Volume – also known as “load testing” – tests the system with large amounts of data that meet or exceed its design load.
Fault Seeding – tests in which a fault is intentionally introduced to the system to ensure the system handles it properly.
Regression tests – normally a subset of previously passed tests to ensure that modification to a system did not introduce errors into previously correctly functioning systems.

## Slide 26: Common testing strategies
“printf” testing – tests the system by writing to a file or to stdout
“Test buddies” – writing test fixtures that embed the test cases in their own functionality
Testing on host – performing most of the tests on the host platforms using a host native complier and a critical subset on the target platform using a cross compiler
Simulating on host – simulating the target platform on the host with cross-compiled software and retesting a critical subset on the target with the same object code
Commercial software testing tools – using software testing tools, such as TestRT, LDRA, or VectorCAST.
Commercial hardware-software integrated tools – this includes tools such as logic analyzers, in-circuit emulators, JTAG-compliant testing tools, and ROM emulators

## Slide 27: Object oriented or Structured?
Structured programming is a disciplined form of software development that emphasizes two separate and distinct aspects.
On one hand, functions or procedures form the foundation of behavioral programming: a procedure is a collection of primitive actions with a single entry point that performs a coherence behavioral goal; a function is simply a procedure that returns a value.
Procedures can be broken up into call trees by one procedure invoking another, permitting algorithmic decomposition.
Procedures are usually synchronously invoked (i.e., called) but by adding additional means, asynchronous invocations can be invoked as well.

## Slide 28: Object oriented or Structured?
The other side of structured programming is the notion of data structuring. All third generation computer languages have the notion of building complex data structures from more primitive elements, ultimately basing them on the basic types provided by the computer language. These may be homogeneous collections, such as arrays, or heterogeneous ones, as with C structs.
Object-oriented programming is based on an orthogonal paradigm. Rather than have two separate taxonomies, object-oriented programming has a single one based on the notion of a class.
A class combines together both data (stored in attributes) and procedures (known as operations) that operate on that data, because they tend to be inherently tightly bound anyway.

## Slide 29: Object oriented or Structured?
An object is an instance of a class. This makes an object equivalent to, but more powerful than, a variable in a structured language because the object provides both the values held in its attributes and the operations that manipulate them.
C is clearly a structured language. C is by far the most prevalent language for creating embedded systems and C is an inherently “structured” language.
However, an interesting question arises: can object-oriented programming be done in a structured language, such as C? And even if it can be done, should it be done?

## Slide 30: Object oriented or Structured?
The creation of object-based or object-oriented programs in C is pretty straightforward.
Let’s briefly discuss the important aspects of object-oriented programming and how to implement those concepts in C.

## Slide 31: Object oriented or Structured?
A class is really nothing more than a C struct, but what is special about it is that it contains two different kinds of features: data (attributes) and behavioral (operations).
The simplest way to implement classes is simply to use the file as the encapsulating boundary; public variables and functions can be made visible in the header file, while the implementation file holds the function bodies and private variables and functions.
In this case, a “class” is represented as a pair of files and its implementation uses some features (variables or functions) of the Display class (file), in this case, the displayMsg() function.

## Slide 32
This allows us to have multiple instances (objects) of the same class and make sure that the member functions work on the correct copies of the data.
In addition, classes are endowed with “special” operations.
A constructor creates an object of the class.
An initializer (optionally) initializes the object and its attributes.
A destructor destroys the class and releases the memory used.

## Slide 33: Example – sensor.h
  #ifndef Sensor_H
  #define Sensor_H
  /*## class Sensor */
  typedef struct Sensor Sensor;
  struct Sensor {
    int filterFrequency;
    int updateFrequency;
    int value;
  };
  int Sensor_getFilterFrequency(const Sensor* const me);
  void Sensor_setFilterFrequency(Sensor* const me, int p_filterFrequency);
  int Sensor_getUpdateFrequency(const Sensor* const me);
  void Sensor_setUpdateFrequency(Sensor* const me, int p_updateFrequency);
  int Sensor_getValue(const Sensor* const me);
  Sensor * Sensor_Create(void);
  void Sensor_Destroy(Sensor* const me);

## Slide 34: sensor.c
#include "Sensor.h"
void Sensor_Init(Sensor* const me) {
}
void Sensor_Cleanup(Sensor* const me) {
}
int Sensor_getFilterFrequency(const Sensor* const me) {
return me->filterFrequency;
}
void Sensor_setFilterFrequency(Sensor* const me, int p_filterFrequency) {
me->filterFrequency = p_filterFrequency;
}
int Sensor_getUpdateFrequency(const Sensor* const me) {
return me->updateFrequency;
}
void Sensor_setUpdateFrequency(Sensor* const me, int p_updateFrequency) {
me->updateFrequency = p_updateFrequency;
}

## Slide 35: sensor.c
int Sensor_getValue(const Sensor* const me) {
return me->value;
}
Sensor * Sensor_Create(void) {
Sensor* me = (Sensor *) malloc(sizeof(Sensor));
if(me!=NULL)
{
Sensor_Init(me);
}
return me;
}
void Sensor_Destroy(Sensor* const me) {
if(me!=NULL)
{
Sensor_Cleanup(me);
}
free(me);
}

## Slide 36
In this case, the file serves as the encapsulation boundary, and stylistically two files (a header .h file and an implementation .c file) group together the elements within a single class.
This approach supports object-based programming very well, but doesn’t implement virtual functions in a fashion that can be easily overridden in subclasses.
An alternative approach that supports object-oriented programming is to embed function pointers within the struct itself.

## Slide 37: Objects
Objects are instances of classes, in the same way that a specific variable x (of type int) is an instance of its type (int).
The same set of operators (such as arithmetic operators) apply to all variables of that type, but the specific values of one instance differ from another instance (say, y).
In standard C programming, complex algorithms can still be embedded in classes, but it is common that these classes are singletons, meaning that there is exactly one instance of the class in the application.
A singleton Printer class, for example, may have variables such as currentPrinter and operations like print(), but the application would have only a single instance. There are still benefits to encapsulating the data used by a class with the operations that act on that data, even if there is only one instance ever running.
In other cases, usually more data-centric (as opposed to algorithm- or service-centric) classes will have multiple instances.

## Slide 38
To create an instance of a class, simply create an instance of the struct. Consider one possible main() that creates and uses two instances of the previous Sensor class

## Slide 39
#include "Sensor.h"
#include <stdlib.h>
#include <stdio.h>
int main(int argc, char* argv[]) {
  Sensor * p_Sensor0, * p_Sensor1;
  p_Sensor0 = Sensor_Create();
  p_Sensor1 = Sensor_Create();
  /* do stuff with the sensors ere */
  p_Sensor0->value = 99;
  p_Sensor1->value = -1;
  printf("The current value from Sensor 0 is %d\n",
  Sensor_getValue(p_Sensor0));
  printf("The current value from Sensor 1 is %d\n",
  Sensor_getValue(p_Sensor1));
  /* done with sensors */
  Sensor_Destroy(p_Sensor0);
  Sensor_Destroy(p_Sensor1);
  return 0;
}

## Slide 40: Polymorphism and Virtual Functions
Polymorphism is a valuable feature of object-oriented languages.
It allows for the same function name to represent one function in one context and another function in a different context.
In practice, this means that when either the static or dynamic context of an element changes, the appropriate operation can be called.
The standard way to do this in C is to use conditional statements such as if or switch.
The problem with the standard approach is that it quickly becomes unwieldy when many different contexts are available.

## Slide 41
Additionally, the approach requires that all possible contexts must be known when the original function is written, or at least the function must be modified to allow a new context.
With polymorphic functions, prescience isn’t required. When the new context is discovered, the polymorphic function may be created and added without requiring changes to the original function.

## Slide 42
int acquireValue(Sensor *me) {
int *r, *w; /* read and write addresses */
int j;
switch(me->whatKindOfInterface) {
  case MEMORYMAPPED:
    w = (int*)WRITEADDR; /* address to write to sensor */
    *w = WRITEMASK; /* sensor command to force a read */
    for (j=0;j<100;j++) { /* wait loop */ };
    r = (int *)READADDR; /* address of returned value */
    me->value = *r;
    break;
  case PORTMAPPED:
    me->value = inp(SENSORPORT);
    /* inp() is a compiler-specific port function */
    break;
}; /* end switch */
return me->value;
};
Consider a sensor in which the actual interface may differ. The acquireValue function in one context may require accessing a memory-mapped sensor, waiting for a while and then reading a different address to acquire the value.
A different context may use a portmapped sensor. We would definitely prefer that the client of the sensor doesn’t know how the interface to the sensor works – requiring such knowledge makes the application far more fragile and difficult to maintain.
With the standard C approach, we’d write code with the attributes whatKindOfInterface added to the Sensor struct.

## Slide 43: Polymorphism and Virtual Functions
Polymorphism is a valuable feature of object-oriented languages.
It allows for the same function name to represent one function in one context and another function in a different context.
In practice, this means that when either the static or dynamic context of an elementchanges, the appropriate operation can be called.
Of course, the standard way to do this in C is to use conditional statements such as if or switch.
The problem with the standard approach is that it quickly becomes unwieldy when many
different contexts are available. Additionally, the approach requires that all possible contexts
must be known when the original function is written, or at least the function must be modified
to allow a new context. With polymorphic functions, prescience isn’t required. When the new
context is discovered, the polymorphic function may be created and added without requiring
changes to the original function.

## Slide 44: Polymorphism and Virtual Functions
Polymorphism is a valuable feature of object-oriented languages.
It allows for the same function name to represent one function in one context and another function in a different context.
In practice, this means that when either the static or dynamic context of an element changes, the appropriate operation can be called.
Of course, the standard way to do this in C is to use conditional statements such as if or switch.
The problem with the standard approach is that it quickly becomes unwieldy when many
different contexts are available. Additionally, the approach requires that all possible contexts
must be known when the original function is written, or at least the function must be modified
to allow a new context. With polymorphic functions, prescience isn’t required. When the new
context is discovered, the polymorphic function may be created and added without requiring
changes to the original function.